CONVERT
                          Version 3.0
                         July  9, 1993

      Copyright (c) 1993  Covox, Inc.  All Rights Reserved

INTRODUCTION

Different sound cards and software often make use of different and
incompatible formats for files they use to record sounds on disk. 
Convert offers a way to translate sound files between several common
formats.


GENERAL DESCRIPTION

CONVERT can understand all Covox sound file formats as well as .VOC
and .WAV files.  It can translate these formats to any of the formats
it understands, except .VMD and .VMF files.

CONVERT has two mode of operation. If run without any command line
parameters, it operates in "menu mode".  Menu mode allows the easy
selection of files to convert using a point and shoot type of
interface.

CONVERT can also be run completely from the command line, allowing
easy use from within batch files, or quick "one shot" conversions for
which menus are unnecessary.


When Covert is started in menu mode, a list of options will be
displayed horizontally across the top of the screen.  These
selections are arranged, from left to right, in the order they are
likely to be used.  You can navigate the selections using the cursor
keys on your keyboard to move the highlight through the selections.
When the selection you want is highlighted, press <Return>.  Pressing
<Esc> at any time backs you out of the current menu.

The main menu selections are:

OPTIONS:        Selecting this brings up a submenu of a number of
                parameters that will affect any conversions made.
                The parameters listed here are:

                Playback Rate:  Selecting this allows you to specify
                        the speed at which the converted files will
                        be played back.  This rate is specified in
                        Hertz. Specifying zero for this option tells
                        CONVERT to keep the same playback rate as in
                        the original file.  NOTE:  Not all possible
                        rates can be specified, so after you enter a
                        value here, it will be changed to match the
                        closest valid value.
                Silence Threshold:  This only has an effect when you
                        are converting to a format with Silence
                        encoding.  This value can be from 0 to 5, and
                        specifies how many units from dead silence 
                        CONVERT will still consider as silence.

                Treble Output:  This toggles between 'Y' and 'N',
                        telling CONVERT to add more treble to the
                        resulting file.  Only effective when
                        converting from .V4S, .V3S, and .V2S file
                        formats.

                Noise Fill:  This toggles between 'Y' and 'N', and is
                        only effective when converting from .V4S,
                        .V3S, and .V2S file formats.  Causes silence
                        to be replaced by low level noise.

                Dest. Path:  Specifies the directory the resulting
                        converted files are to be placed in.  This
                        defaults to the directory you are in when you
                        run CONVERT.  The current destination path is
                        always displayed at the bottom of the screen.

FILE MASKS:     By default, CONVERT will only see files with
                extensions representing the file formats it knows. 
                You can change the file masks in this menu.  A file
                mask is a list of file masks, separated by commas,
                semicolons, or spaces.  If a file name matches any of
                the file masks on this list, it will be displayed in 
                the directory window.

SORTING:        This allows the directory window to be sorted
                according to your tastes. Has no other effect on the
                program's operation.

FORMAT:         This brings up a menu allowing you to specify which
                format you wish to convert to.  The current target
                format is always displayed at the bottom of the
                screen

CONVERT:        Brings up a menu to perform the actual conversions: 
                The menu has three options:

                Select files to convert:  When you pick this, a
                  highlight bar will appear in the directory window. 
                  This bar can be moved around using the cursor keys. 
                  You then need to select which files you want to
                  convert by moving the highlight to them, and pressing
                  either <Return> or the spacebar.  A check mark will
                  appear next to the file name to indicate that you
                  have selected that file.  If you mistakenly select
                  the wrong file, pressing <Return> on it again will
                  deselect it.

                  Names that appear in angle brackets ( < and > ) are
                  directories.  Pressing <Return> on these changes the
                  directory  being displayed.  You can select any
                  number of files, in any directories you wish.  When
                  you have selected all the files you want to convert,
                  press <Esc>.

                Convert All Selected Files:  Selecting this item will
                  initiate the conversion off all the files you have
                  selected using the "Select Files to Convert" option.

                Exit Convert:   This is the same as pressing <Esc>
                  from the main menu, allowing you to leave the
                  program.
                        


                 CONVERT Sound File Conversion Utility
                              Version 3.0
                             July  9, 1993


SYNTAX : CONVERT [/<switches>] [<filespec> [<filespec>] ...]

OPTIONS:

        /Fxxx - Specify output format. 'xxx' can be one of:
                     8  - 8 bit PCM               2S  - 2 bit ADPCM w/silence
                     8S - 8 bit PCM w/silence     VOC - 8 bit PCM
                     4S - 4 bit ADPCM w/silence   WAV - 8 bit PCM
                     3S - 3 bit ADPCM w/silence
        /N    - Replace silence w/noise (when reading V8S, V4S, V3S, V2S)
        /Rxxx - Set the sampling rate of the new file
        /Sx   - Set the silence thresh. (when making V4S, V3S, and V2S files
        /T    - Turn on treble (when reading V4S, V3S, and V2S files)
        /B    - Use BIOS for video access (use this if menus don't work right)
        /?    - Display help screen.
        
        
        Example: CONVERT /N /F3S *.*
           Converts all files in current dirctory to V3S format, replacing
           encoded silence with noise.